## Slide 1: Chapter 5 Network Layer: The Control Plane
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify,
and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this
material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top Down Approach
7th edition
Jim Kurose, Keith Ross
Pearson/Addison Wesley April 2016

## Slide 2: Chapter 5: network layer control plane
chapter goals: understand principles behind network control plane
traditional routing algorithms
SDN controlllers
Internet Control Message Protocol
network management
and their instantiation, implementation in the Internet:
OSPF, BGP, OpenFlow, ODL and ONOS controllers, ICMP, SNMP

## Slide 3: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 4: Network-layer functions
data plane
control plane
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
Recall: two network-layer
fufnocrwtioarndsin:g: move packets
from router’s input to appropriate router output
routing: determine route taken by packets from source to destination

## Slide 5: Per-router control plane (Traditional Way)
Routing Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data plane
control plane

## Slide 6: Logically centralized control plane
control plane
data plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 7: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 8: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!

## Slide 9: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g., P2P, where N is set of peers and E is set of TCP connections

## Slide 10: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or inversely related to bandwidth, or inversely related to congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 11: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically- connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes
Network Layer: Control Plane 5-11

## Slide 12: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 13: A link-state routing algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 14: Dijsktra’s algorithm
1 Initialization:
2 N' = {u}
for all nodes v
if v adjacent to u
then D(v) = c(u,v)
else D(v) = ∞ 7
Loop
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' : 12 D(v) = min( D(v), D(w) + c(w,v) )
/* new cost to v is either old cost to v or known
shortest path cost to w plus cost from w to v */
15 until all nodes in N'
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 15: Dijkstra’s algorithm: example
Network Layer
4-15
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
2,u
D(v),p(v) D(w),p(w)
2,u 5,u
2,u 4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(v) = min( D(v), D(w) + c(w, v) )
x
v x v
2
1
2
Formula: D(v) = min( D(v), D(w) + c(w, v) )
D(v) = min( D(v), D(w) + c(w, v) )
5
1
3
w U to w
x x w
U to x
D(v) = min( D(v), D(w) + c(w, v) )
∞
1
1
y U to y
x x y
U to x
resulting shortest-path tree from u:
D(v) = min( D(v), D(w) + c(w,v) )
/* new cost to v is either old cost to v or known shortest path cost to w plus cost from w to v */

## Slide 16: Dijkstra’s algorithm: example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
5
D(v) D(w) D(x) D(y) D(z)
Step N' |  | p(v) | p(w) | p(x) | p(y) | p(z)
0 | u | 7,u | 3,u | 5,u | ∞ | ∞
1 | uw | 6,w |  | 5,u | 11,w | ∞
2 | uwx | 6,w |  |  | 11,w | 14,x
3 | uwxv |  |  |  | 10,v | 14,x
4 uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz
Network Layer: Control Plane 5-16

## Slide 17: Dijkstra’s algorithm: another example
Step | N' | D(v),p(v) | D(w),p(w) | D(x),p(x) | D(y),p(y) | D(z),p(z) | 
0 | u | 2,u | 5,u | 1,u | ∞ | ∞ | 
1
2
3
4
5
ux
uxy
uxyv
uxyvw
uxyvwz
2,u
2,u
4,x
3,y
3,y
2,x
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Network Layer: Control Plane 5-17
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 18: Dijkstra’s algorithm: example (2)
u
y
x
z
resulting shortest-path tree from u:
v w
v (u,v)
(u,x)
(u,x)
w (u,x)
z (u,x)
destination
link
resulting forwarding table in u:

## Slide 19: Dijkstra’s algorithm, discussion
algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
oscillations possible:
e.g., support link cost equals amount of carried traffic:
A
D
C
B
1 1+e
e
0
1
1
0 0
e
initially
B
0
2+e
D
0
1+e 1
C
B
0 2+e
1+e
0
D
1
0 0
C
A A A
B
given these costs, given these costs, given these costs,
find new routing…. find new routing…. find new routing….
resulting in new costs resulting in new costsresulting in new costs
0
0
2+e
D
0
1+e 1
C

## Slide 20: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 21: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y then
dx(y) = min {c(x,v) + dv(y) }
v
cost from neighbor v to destination y cost to neighbor v
min taken over all neighbors v of x

## Slide 22: Bellman-Ford example
u
y
x
v w
z
2
2
1
3
1
1
2
5
3
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
Let’s check the validity of B-F eq: Let’s check it for
Source node u and destination node z; the source node u has 3 neighbors: v, x, w
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
Cost from neighbor v to dest z

## Slide 23: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains
Dv = [Dv(y): y є N ]

## Slide 24: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate
Dx(y) converge to the actual least cost dx(y)

## Slide 25: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
each node:
wait for (change in local link cost or msg from neighbor)
recompute estimates if DV to any dest has
changed, notify neighbors

## Slide 26
Network Layer
4-26

## Slide 27
x y z
x 0 2 7
y ∞ ∞ ∞
z ∞ ∞ ∞
from
cost to
from
from
x y z
x y z
cost to
x y z
x y z
∞ ∞ ∞
7 1 0
cost to
x ∞ ∞ ∞ y
z
2 0 1
∞ ∞ ∞
∞ ∞ ∞
x
z
1
2
7
y
node x table
x
D (y) = min{c(x,y) + D (y), c(x,z) + D (y)}
y z
= min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) +
Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
0 2 3
2 0 1
7 1 0
time
Network Layer: Control Plane 5-27
node y table
node z table
cost to
x y z
from

## Slide 28
from
cost to
x y z
from
cost to
x y z
from
cost to
x y z
x y z
from
cost to
x y z
from
cost to
x 0 2 7
y 2 0 1
z 7 1 0
x 0 2 7
y 2 0 1
z 3 1 0
x 0 2 3
y 2 0 1
z 3 1 0
x 0 2 3
y 2 0 1
z 3 1 0
x 0 2 3
y 2 0 1
z 3 1 0
x y z
x 0 2 7
y ∞ ∞ ∞
z ∞ ∞ ∞
from
cost to
from
from
x y z
x y z
cost to
x y z
x y z
∞ ∞ ∞
7 1 0
cost to
x ∞ ∞ ∞ y
z
2 0 1
∞ ∞ ∞
∞ ∞ ∞
x
z
1
2
7
y
node x table
x
D (y) = min{c(x,y) + D (y), c(x,z) + D (y)}
y z
= min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) +
Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
0 2 3
2 0 1
7 1 0
time
Network Layer: Control Plane 5-27
node y table
node z table
cost to
x y z
from

## Slide 29: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
“good
news travels fast”
x
z
1
4
50
y
1
if DV ct h:ayndgeteecst,s nlinokt-icfoystncehiagnhgeb,ourpsdates its DV, informs its
0
neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.
Network Layer: Control Plane 5-29
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 30: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm
stabilizes: see text
x
z
1
50
y
60
4
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?

## Slide 31: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
DV:
robustness: what happens if router malfunctions?
LS:
node can advertise incorrect link cost
each node computes only its own table
DV node can advertise incorrect path cost
each node’s table used by others
  error propagate thru network

## Slide 32: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 33: Making routing scalable
scale: with billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 34: Internet approach to scalable routing aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter- domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run
same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
Network Layer: Control Plane 5-34

## Slide 35: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS Routing algorithm
Inter-AS Routing algorithm
Forwarding
table
3c
forwarding table configured by both intra
  and inter-AS routing
algorithm
    intra-AS routing determine entries for destinations within AS
    inter-AS & intra-AS determine entries for exteNrentwaorkl Ldayeers: Ctoinntroal Ptliaonen5s-35

## Slide 36: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS2
3b
AS3
3c
3a
1c
1a AS1
1d
1b
2a
2c
2b
other networks
other networks

## Slide 37: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First (IS-IS protocol essentially same as OSPF)
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)

## Slide 38: OSPF (Open Shortest Path First)
“open”: publicly available
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
  link state: for each attached link
IS-IS (intermediate System to Intermediate System) routing protocol: nearly identical to OSPF

## Slide 39: OSPF “advanced” features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 40: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area border routers
internal routers

## Slide 41: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’es.

## Slide 42: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 43: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 44: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2a
3b
3d
3c
AS 2
AS 3
AS 1
1c
2∂c
3∂a
gateway routers run both eBGP and iBGP protools

## Slide 45: BGP basics
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement: AS3, X

## Slide 46: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 47: BGP path advertisement
1b
1d
1c
1a
2b
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
2d
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 48: BGP path advertisement
1b
1d
1c
1a
2b
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
2d
gateway router may learn about multiple paths to destination:
AS1 gateway router 1c learns path AS2,AS3,X from 2a
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path
AS3,X, and advertises path within AS1 via iBGP

## Slide 49: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 50: BGP, OSPF, forwarding table entries
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
X
AS3,X
AS2,AS3,X
AS3,X
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through
1cd”: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
AS1
1
2
dest
interface
…
X
…
… 1
…
physical link
local link interfaces at 1a, 1d

## Slide 51: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
X
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
X
…
… 2
…
1d”: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface
2
AS1
1
2
Network Layer: Control Plane 5-51

## Slide 52: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 53: Hot Potato Routing
1b
1d
1c
1a
2b
2d
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
112
2c
152
263

## Slide 54: BGP: achieving policy via advertisements
A
C
W
X
legend:
B
customer network:
provider network
Y
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w

## Slide 55: BGP: achieving policy via advertisements
.. so X will not advertise to B a route to C
A
C
W
X
legend:
B
customer network:
provider network
Y
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
Network Layer: Control Plane 5-55

## Slide 56: Why different Intra-, Inter-AS routing
?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance

## Slide 57: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 58: Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 59: Recall: per-router control plane
Routing Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data plane
control plane

## Slide 60: Recall: logically centralized control plane
control plane
data plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 61: Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming: more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane

## Slide 62: Analogy: mainframe to PC evolution*
App
Specialized Applications
Specialized Operating System
Specialized Hardware
Microprocessor
Open Interface
Linux
Mac OS
Windows
(OS)
or or
Open Interface
Vertically integrated Closed, proprietary Slow innovation Small industry
* Slide courtesy: N. McKeown
Horizontal Open interfaces Rapid innovation
Huge industry
Network Layer: Control Plane 5-62

## Slide 63: Traffic engineering: difficult traditional routing
Q: what if network operator wants u-to-z traffic to flow along
uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Link weights are only control “knobs”: wrong!
2
2
1
3
1
1
2
5
3
5
v w
u
z
y
x

## Slide 64: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x

## Slide 65: Traffic engineering: difficult
y
x
2
2
1
3
1
1
2
5
3
5
u
vv
x
ww
y
zz
Q: what if w wants to route blue and red traffic differently?
A: can’t do it (with destination based forwarding, and LS, DV routing)
Networking 401

## Slide 66: Software defined networking (SDN)
control plane
data plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized“ flow- based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane
functions external to data- plane switches
…
4. programmable
control
applications
routing
access control
load balance

## Slide 67: SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data plane
SDN-controlled switches
network-control applications
…
routing
access load control balance
control
northbound API plane
SDN Controller
(network operating system)
southbound API
Network Layer: Control Plane 5-67

## Slide 68: SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network
control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed
system for performance, scalability, fault-tolerance, robustness
data plane
control plane
SDN Controller
(network operating system)
southbound API
northbound API
SDN-controlled switches
network-control applications
…
routing
access load control balance
Network Layer: Control Plane 5-67

## Slide 69: SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data plane
control plane
…
routing
access control
load balance
northbound API
SDN Controller
(network operating system)
southbound API
SDN-controlled switches
network-control applications
Network Layer: Control Plane 5-67

## Slide 70: Components of SDN controller
Network-wide distributed, robust state management
Communication to/from controlled devices
switch info
Link-state info host info
statistics flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful API
…
Interface, abstractions for network control apps
SDN
controller
routing access load
control balance
Interface layer to network control apps: abstractions API
Network-wide state management layer: state of networks links, switches, services: a distributed
database communication layer:
communicate
between SDN controller and controlled switches

## Slide 71: OpenFlow protocol
operates between
controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)
OpenFlow Controller

## Slide 72: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of
OpenFlow Controller
Network Layer: Control Plane 5-72
specific switch port

## Slide 73: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly.
Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 74: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
OpenFlow
SNMP
…
network graph
intent
RESTful API
…
…
1
2
3
4
6
5
Dijkstra’s link-state Routing
s1
s2
s3
s4
S1, experiencing link failure using OpenFlow port status message to notify controller
1
2
SDN controller receives OpenFlow message, updates link status info
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes

## Slide 75: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
OpenFlow
SNMP
…
network graph
intent
RESTful API
…
…
2
3
4
6
5
Dijkstra’s link-state Routing
s1
1
s2
s3
s4
5
link state routing app interacts with flow-table- computation component in SDN controller, which computes new flow tables needed
Controller uses OpenFlow to install new tables in switches that need updating
6

## Slide 76: OpenDaylight (ODL) controller
topology manager
REST API
Basic Network Service Functions
OpenFlow 1.0
…
SNMP
OVSDB
forwarding manager
switch manager
host manager
stats manager
Network service apps
Service Abstraction Layer (SAL)
Access Control
Traffic …
Engineering
ODL Lithium controller
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services

## Slide 77: ONOS controller
Network control apps
…
REST API
southbound abstractions, protocols
OVSDB
device link
OpenFlow
host
Netconf
flow
packet
northbound abstractions, protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
ONOS
distributed core
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling

## Slide 78: SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: “baked in” from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling

## Slide 79: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 80: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type | Code | description
0 | 0 | echo reply (ping)
3 | 0 | dest. network unreachable
3 | 1 | dest host unreachable
3 | 2 | dest protocol unreachable
3 | 3 | dest port unreachable
3 | 6 | dest network unknown
3 | 7 | dest host unknown
4 | 0 | source quench (congestion
 |  | control - not used)
8 | 0 | echo request (ping)
9 | 0 | route advertisement
10 | 0 | router discovery
11 | 0 | TTL expired
12 | 0 | bad IP header
Network Layer: Control Plane 5-80

## Slide 81: Traceroute and ICMP
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
3 probes
3 probes
3 probes

## Slide 82: Chapter 5: outline
  introduction
  routing protocols
link state
distance vector
  intra-AS routing in the Internet: OSPF
  routing among the ISPs: BGP
  The SDN control plane
  ICMP: The Internet Control Message Protocol
  Network management and SNMP

## Slide 83: What is network management?
autonomous systems (aka “network”): 1000s of interacting hardware/software components
other complex systems requiring monitoring, control:
  jet airplane
  nuclear power plant
  others?
"Network management includes the deployment, integration and coordination of the hardware, software, and human elements to monitor, test, poll, configure, analyze, evaluate, and control the network and element resources to meet the real-time, operational performance, and Quality of Service requirements at a reasonable cost."

## Slide 84: Infrastructure for network management
managed device
managed device
managed device
managed device
definitions:
managed devices contain managed objects whose data is gathered into a Management Information Base (MIB)
managing entity
data
managing entity
agent data
agent data
network management
protocol
managed device
agent data
agent data
agent data

## Slide 85: SNMP protocol
Two ways to convey MIB info, commands:
agent data
managed device
managing entity
agent data
managed device
managing entity
trap msg
request
request/response mode
trap mode
response

## Slide 86: SNMP protocol: message types
Message type
GetRequest GetNextRequest GetBulkRequest
Function
manager-to-agent: “get me data”
(data instance, next data in list, block of data)
InformRequest
manager-to-manager: here’s MIB value
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to Request
Trap
Agent-to-manager: inform manager of exceptional event

## Slide 87: SNMP protocol: message formats
….
PDU
type (0-3)
Request ID
Error Status (0-5)
Error Index
Name
Value
Name
Value
….
PDU
type 4
Enterprise
Agent Addr
Trap Type (0-7)
Specific code
Time stamp
Name
Value
Get/set header Variables to get/set
Trap header
Trap info
SNMP PDU
More on network management: see earlier editions of text!

## Slide 88: Chapter 5: summary
we’ve learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF, BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
network management
next stop: link layer!