## Slide 1: Chapter 7 Wireless and Mobile Networks
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify,
and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this
material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top Down Approach
7th edition
Jim Kurose, Keith Ross
Pearson/Addison Wesley April 2016

## Slide 2: Ch. 6: Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers (5-to-1)!
# wireless Internet-connected devices equals # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Chapter 7 outline
  Introduction
Wireless
  Wireless links, characteristics
    CDMA
6.73 IEEE 802.11 wireless LANs (“Wi-Fi”)
  Cellular Internet Access
    architecture
    standards (e.g., 3G, LTE)
Mobility
  Principles: addressing and routing to mobile users
  Mobile IP
  Handling mobility in cellular networks
  Mobility and higher-layer protocols

## Slide 4: Elements of a wireless network
network infrastructure

## Slide 5: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non- mobile) or mobile
  wireless does not
always mean mobility
network infrastructure

## Slide 6: Elements of a wireless
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers,
802.11 access points
network
network infrastructure

## Slide 7: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network infrastructure

## Slide 8: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range outdoor
200m – 4 Km
Long-range outdoor
5Km – 20 Km
.384
.056
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
802.11n
Data rate (Mbps)
1300
450
54
5-11
4
1
802.11 ac

## Slide 9: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network infrastructure

## Slide 10: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 11: Wireless network taxonomy
 | single hop | multiple hops
infrastructure (e.g., APs) no infrastructure | host connects to base station (WiFi, WiMAX, cellular) which connects to larger Internet | host may have to relay through several wireless nodes to connect to larger Internet: mesh net
 | no base station, no connection to larger Internet (Bluetooth, ad hoc nets) | no base station, no connection to larger Internet. May have to relay to reach other a given wireless node MANET, VANET

## Slide 12: Chapter 7 outline
  Introduction
Wireless
  Wireless links, characteristics
    CDMA
  IEEE 802.11 wireless LANs (“Wi-Fi”)
  Cellular Internet Access
    architecture
    standards (e.g., 3G, LTE)
Mobility
  Principles: addressing and routing to mobile users
  Mobile IP
  Handling mobility in cellular networks
  Mobility and higher-layer protocols

## Slide 13: Wireless Link Characteristics (1)
important differences from wired link ….
decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 14: Wireless Link Characteristics (2)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoffs
given physical layer: increase power -> increase SNR-
>decrease BER
given SNR: choose physical layer that meets BER requirement, giving highest thruput
  SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
20
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 15: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal strength
C’s signal strength
space
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 16: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence

## Slide 17: CDMA encode/decode
Zi,m= d .c
i m
 |  |  |  |  |  |  |  | d0 = 1 |  |  |  |  |  |  | 
d1 = -1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 | 1 | 1 |  | 1 |  |  |  | 1 | 1 | 1 |  | 1 |  |  | 
 |  |  | -1 |  | -1 | -1 | -1 |  |  |  | -1 |  | -1 | -1 | -1
slot 1 |  |  |  |  |  |  |  | slot 0 |  |  |  |  |  |  | 
 |  |  | 1 |  | 1 | 1 | 1 | 1 | 1 | 1 |  | 1 |  |  | 
-1 | -1 | -1 |  | -1 |  |  |  |  |  |  | -1 |  | -1 | -1 | -1
slot 1 |  |  |  |  |  |  |  | slot 0 |  |  |  |  |  |  | 
channel output
channel output
channel output Zi,m
sender
code
data bits
 |  |  | 1 |  | 1 | 1 | 1 | 1 | 1 | 1 |  | 1 |  |  | 
-1 | -1 | -1 |  | -1 |  |  |  |  |  |  | -1 |  | -1 | -1 | -1
1 | 1 | 1 |  | 1 |  |  |  | 1 | 1 | 1 |  | 1 |  |  | 
 |  |  | -1 |  | -1 | -1 | -1 |  |  |  | -1 |  | -1 | -1 | -1
slot 1 |  |  |  |  |  |  |  | slot 0 |  |  |  |  |  |  | 
 | d0 = 1
d1 = -1 | 
slot 1 | 
slot 0 channel output
channel output
receiver
code
received input
Di =  Z
.c
i,m m
m=1
M
M

## Slide 18: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions
by sender 1 and 2

## Slide 19: Chapter 7 outline
  Introduction
Wireless
  Wireless links, characteristics
    CDMA
  IEEE 802.11 wireless LANs (“Wi-Fi”)
  Cellular Internet Access
    architecture
    standards (e.g., 3G, LTE)
Mobility
  Principles: addressing and routing to mobile users
  Mobile IP
  Handling mobility in cellular networks
  Mobility and higher-layer protocols

## Slide 20: IEEE 802.11 Wireless LAN
802.11b
2.4-5 GHz unlicensed spectrum
up to 11 Mbps
direct sequence spread spectrum (DSSS) in physical layer
  all hosts use same chipping code
802.11a
5-6 GHz range
up to 54 Mbps
802.11g
2.4-5 GHz range
up to 54 Mbps
  n: multiple antennae
    2.4-5 GHz range
    up to 200 Mbps
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions

## Slide 21: 802.11 LAN architecture
wireless host communicates with base
station
base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch or router

## Slide 22: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames
containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet

## Slide 23: 802.11: passive/active scanning
AP 2
AP 1
BBS 2
BBS 1
1
2
3
1
H1
passive scanning:
beacon frames sent from APs
association Request frame sent:
H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
BBS 2
BBS 1
1
2
2
3
4
H1
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent:
H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 24: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal strength
C’s signal strength

## Slide 25: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
transmit entire frame (no CD) 2 if sense channel busy then
start random backoff time
timer counts down while channel idle transmit when timer expires
if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 26: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely using small reservation packets!

## Slide 27: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 28: 802.11 frame: addressing
2
frame control | duration | address 1 | address 2 | address 3 | seq control | address 4 | payload | CRC
2
2
6
6
6
6
0 - 2312
4
Address 1: MAC address of wireless host or AP
to receive this frame
which AP is attached Address 2: MAC address
of wireless host or AP transmitting this frame
Address 4: used only in ad hoc mode
Address 3: MAC address of router interface to

## Slide 29: 802.11 frame: addressing
Internet
H1
R1 router
 | AP MAC addr | H1 MAC addr | R1 MAC addr | 
address 1
address 2
address 3
802.11 frame
 | R1 MAC addr | H1 MAC addr | 
dest. address
source address
802.3 frame

## Slide 30: 802.11 frame: more
duration of reserved transmission time (RTS/CTS)
2 2 6 6 6 2
frame control | duration | address 1 | address 2 | address 3 | seq control | address 4 | payload | CRC
6
0 - 2312
4
Protocol version | Type | Subtype | To AP | From AP | More frag | Retry | Power mgt | More data | WEP | Rsvd
2
2
4
1
1
1
1
1
1
1
1
frame seq # (for RDT)
frame type
(RTS, CTS, ACK, data)

## Slide 31: 802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1
H1
BBS 2
BBS 1

## Slide 32: 802.11: advanced capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
BER
10-1
10-2
10-3
10-6
10-7
10-4
10-5
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
operating point
10 20 30 40
SNR(dB)
SNR decreases, BER increase as node moves away from base station
When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 33: 802.11: advanced capabilities
power management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame

## Slide 34: 802.15: personal area network
M
radius of coverage
S
S
S
P
P
P
P
M
Master device
S Slave device
P Parked device (inactive)
less than 10 m diameter
replacement for cables
(mouse, keyboard, headphones)
ad hoc: no infrastructure
master/slaves:
  slaves request permission to send (to master)
  master grants requests
802.15: evolved from Bluetooth specification
  2.4-2.5 GHz radio band
  up to 721 kbps

## Slide 35: Chapter 7 outline
  Introduction Wireless
  Wireless links, characteristics
    CDMA
  IEEE 802.11 wireless LANs (“Wi-Fi”)
  Cellular Internet access
    architecture
    standards (e.g., 3G, LTE)
Mobility
  Principles: addressing and routing to mobile users
  Mobile IP
  Handling mobility in cellular networks
  Mobility and higher-layer protocols

## Slide 36: Components of cellular network architecture
Mobile Switching Center
Public telephone network
Mobile Switching Center
handles mobility (more later!)
MSC
connects cells to wired tel. net.
manages call setup (more later!)
covers geographical region
base station (BS)
analogous to 802.11 AP
mobile users
attach to network through BS
air-interface:
physical and link
layer protocol between mobile and BS
cell
wired network
Wireless and Mobile Networks
7-36

## Slide 37: Cellular networks: the first hop
Two techniques for sharing
mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
frequency bands
time slots

## Slide 38: 2G (voice) network architecture
BSC
BTS
Legend
Base transceiver station (BTS) Base station controller (BSC)
Mobile Switching Center (MSC) Mobile subscribers
Base station system (BSS)
MSC
Public
telephone
network
Gateway MSC
G

## Slide 39: 3G (voice+data) network architecture
radio network controller
MSC
SGSN
Public
telephone
network
Gateway MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public Internet
GGSN
G
Key insight: new cellular data network operates in parallel (except at edge) with existing cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 40: 3G (voice+data) network architecture
radio network controller
MSC
SGSN
Public
telephone
network
Gateway MSC
G
Public Internet
GGSN
G
radio access network
Universal Terrestrial Radio Access Network (UTRAN)
core network
General Packet Radio Service (GPRS) Core Network
public Internet
radio interface
(WCDMA, HSPA)

## Slide 41: 3G versus 4G LTE network architectur
radio network controller
MSC
SGSN
Public
telephone
network
Gateway MSC
G
Public Internet
G
GGSN
radio access network
Universal Terrestrial Radio Access Network (UTRAN)
Evolved Packet Core (EPC)
MME
Public Internet
G
S-GW P-GW
G
HSS
3G
4G-LTE

## Slide 42: 4G: differences from 3G
all IP core: IP packets tunneled (through core IP network) from base station to gateway
no separation between voice and data – all traffic carried over IP core to gateway
radio access network
Universal Terrestrial Radio Access Network (UTRAN)
Evolved Packet Core (EPC)
Public Internet
G
S-GW P-GW
G
UE
(user element)(base station)
network Gateway (P-GW)
Serving Packet data
Gateway (S-GW)
data
MME
HSS
Mobility Management Entity (MME)
eNodeB
control
Home Subscriber Server(HSS) (like HLR+VLR)

## Slide 43: Functional split of major LTE components
handles idle/active UE transitions pages UE
sets up eNodeB-PGW tunnel (aka bearer)
holds idle UE info QoS enforcement

## Slide 44: Radio+Tunneling: UE – eNodeB – PGW
Wireless and Mobile Networks 7-44
tunnel
link-layer radio net
UE
eNodeB
S-GW
G
P-GW
G
IP packet from UE encapsulated in GPRS Tunneling Protocol (GTP) message at ENodeB
GTP message encapsulated in UDP, then encapsulated in IP. large IP packet addressed to SGW

## Slide 45: Quality of Service in LTE
QoS from eNodeB to SGW: min and max guaranteed bit rate
QoS in radio access network: one of 12 QCI values

## Slide 46: Chapter 7 outline
  Introduction Wireless
  Wireless links, characteristics
    CDMA
  IEEE 802.11 wireless LANs (“Wi-Fi”)
  Cellular Internet Access
    architecture
    standards (e.g., 3G, LTE)
Mobility
  Principles: addressing and routing to mobile users
  Mobile IP
  Handling mobility in cellular networks
  Mobility and higher-layer protocols

## Slide 47: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user, using same access point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 48: Mobility: vocabulary
wide area network
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
permanent address: address in home network, can always be used to reach mobile e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote

## Slide 49: Mobility: more vocabulary
wide area network
care-of-address: address in visited network.
(e.g., 79,129.13.2)
visited network: network in
which mobile currently resides (e.g., 79.129.13/24)
permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in
visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 50: How do you contact a mobile friend:
expect her to let you know where he/she is?
Facebook!
I wonder where Alice moved to?
Consider friend frequently changing addresses, how do
ysoeuarfcinhdalhl pehr?one books?
call her parents?

## Slide 51: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in- residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 52: Mobility: approaches
located
no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile
let routing handle it: routers advertise permanent addressnootf mobile-nodes-in- residence via ususaclalraobuleting table exchange.
routing tablestoinmdililcioansteofwhere each mobile
mobiles

## Slide 53: Mobility: registration
end result:
foreign agent knows about mobile
home agent knows location of mobile
home network
visited network
1
mobile contacts foreign agent on entering visited network
wid2e area network
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 54: Mobility via indirect routing
home network
visited network
3
wide area networ2k
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 55: Indirect Routing: comments
mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
foreign agent functions may be done by mobile itself
triangle routing: correspondent-home-network- mobile
  inefficient when correspondent, mobile are in same network

## Slide 56: Indirect routing: moving between networks
suppose mobile user moves to another network
  registers with new foreign agent
  new foreign agent registers with home agent
  home agent update care-of-address for mobile
  packets continue to be forwarded to mobile (but with new care-of-address)
mobility, changing foreign networks transparent: on going connections can be maintained!

## Slide 57: Mobility via direct routing
2
4
correspondent forwards to foreign agent
home network
1
correspondent requests, receives foreign address of mobile
foreign agent receives packets, forwards to mobile
visited
network
3
mobile replies directly to correspondent

## Slide 58: Mobility via direct routing: comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?
1
2
3
4

## Slide 59: Accommodating mobility with direct routing
wide area network
1
agent
2
new foreign agent
3
correspondent agent
correspondent
new foreign network
anchor foreign agent: FA in first visited network
data always routed first to anchor FA
when mobile moves: new FA arranges to have data forwarded from old FA (chaining)
foreign net visited
at session start
anchor foreign
4
5

## Slide 60: Chapter 7 outline
  Introduction Wireless
  Wireless links, characteristics
    CDMA
  IEEE 802.11 wireless LANs (“Wi-Fi”)
  Cellular Internet Access
    architecture
    standards (e.g., 3G, LTE)
Mobility
  Principles: addressing and routing to mobile users
  Mobile IP
  Handling mobility in cellular networks
  Mobility and higher-layer protocols

## Slide 61: Mobile IP
RFC 3344
has many features we’ve seen:
  home agents, foreign agents, foreign-agent registration, care-of-addresses, encapsulation (packet-within-a-packet)
three components to standard:
  indirect routing of datagrams
  agent discovery
  registration with home agent

## Slide 62: Mobile IP: indirect routing
Permanent address: 128.119.40.186
Care-of address: 79.129.13.2
dest: 128.119.40.186
packet sent by correspondent
packet sent by home agent to foreign agent: a packet within a packet
dest: 79.129.13.2 dest: 128.119.40.186
foreign-agent-to-mobile packet
dest: 128.119.40.186

## Slide 63: Mobile IP: agent discovery
agent advertisement: foreign/home agents advertise service by broadcasting ICMP messages (typefield = 9)
H,F bits: home and/or foreign agent
R bit: registration required

## Slide 64: Mobile IP: registration
example
home agent HA: 128.119.40.7
visited network: 79.129.13/24 foreign agent
COA: 79.129.13.2
mobile agent
MA: 128.119.40.186
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999 identification:714
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714 encapsulation format
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714
….
time
ICMP agent
adv.
COA: 79.129.13.2
….
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999
identification: 714 encapsulation format
….

## Slide 65: Components of cellular network architecture
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone network
different cellular networks, operated by different providers
recall:

## Slide 66: Handling mobility in cellular networks
home network: network of cellular provider you subscribe to (e.g., Sprint PCS, Verizon)
  home location register (HLR): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
visited network: network in which mobile currently resides
  visitor location register (VLR): database with entry for each user currently in network
  could be home network

## Slide 67: GSM: indirect routing to mobile
Public switched telephone network
mobile user
home Mobile Switching Center
HLR
home network
visited network
correspondent
Mobile Switching Center
VLR
1
call routed
to home network
2
home MSC consults HLR, gets roaming number of mobile in visited network
3
home MSC sets up 2nd leg of call to MSC in visited network
4
MSC in visited network completes call through base station to mobile

## Slide 68: GSM: handoff with common MSC
Mobile
Switching Center
VLR
old BSS
new BSS
old routing
new routing
handoff goal: route call via new base station (without interruption)
reasons for handoff:
stronger signal to/from new BSS (continuing connectivity, less battery drain)
load balance: free up channel in current BSS
GSM doesn't mandate why to perform handoff (policy), only how (mechanism)
handoff initiated by old
BSS
Wireless and Mobile Networks 7-68

## Slide 69: GSM: handoff with common MSC
Mobile Switching
VLR
old BSS
1
3
Center 2
4
5
6
7
8
new BSS
old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
MSC sets up path (allocates resources) to new BSS
new BSS allocates radio channel for use by mobile
new BSS signals MSC, old BSS: ready
old BSS tells mobile: perform handoff to new BSS
mobile, new BSS signal to activate new channel
mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
8 MSC-old-BSS resources released

## Slide 70: GSM: handoff between MSCs
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(a) before handoff
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
optional path minimization step to shorten multi-MSC chain

## Slide 71: GSM: handoff between MSCs
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
(b) after handoff
anchor MSC: first MSC
visited during call
call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
optional path minimization step to shorten multi-MSC chain
MSC

## Slide 72: Handling Mobility in LTE
Paging: idle UE may move from cell to cell: network does not know where the idle UE is resident
  paging message from MME broadcast by all
eNodeB to locate UE
handoff: similar to 3G:
  preparation phase
  execution phase
  completion phase
P-GW
old
eNodeB
old routing
new routing
new
eNodeB
source MME
target MME

## Slide 73: Mobility: cellular versus Mobile IP
cellular element Comment on cellular element Mobile IP element |  | 
Home system | Network to which mobile user’s permanent phone number belongs | Home network
Gateway Mobile Switching Center, or “home MSC”. Home Location Register (HLR) | Home MSC: point of contact to obtain routable address of mobile user. HLR: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information | Home agent
Visited System | Network other than home system where mobile user is currently residing | Visited network
Visited Mobile services Switching Center. Visitor Location Record (VLR) | Visited MSC: responsible for setting up calls to/from mobile nodes in cells associated with MSC. VLR: temporary database entry in visited system, containing subscription information for each visiting mobile user | Foreign agent
Mobile Station Roaming Number (MSRN), or “roaming number” | Routable address for telephone call segment between home MSC and visited MSC, visible to neither the mobile nor the correspondent. | Care-of- address

## Slide 74: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links

## Slide 75: Chapter 7 summary
Wireless
wireless links:
  capacity, distance
  channel impairments
  CDMA
IEEE 802.11 (“Wi-Fi”)
  CSMA/CA reflects wireless channel characteristics
cellular access
  architecture
  standards (e.g., 3G, 4G LTE)
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile IP
  mobility in GSM, LTE
impact on higher-layer protocols