## Slide 1: Chapter 9 Multimedia Networking
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify,
and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this
material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top Down Approach
7th edition
Jim Kurose, Keith Ross
Pearson/Addison Wesley April 2016
Multimedia Networking 9-1

## Slide 2: Multimedia networking: outline
  multimedia networking applications
  streaming stored video
  voice-over-IP
  protocols for real-time conversational applications
  network support for multimedia
Multimedia Networking 9-1

## Slide 3: Multimedia: audio
analog audio signal sampled at constant rate
  telephone: 8,000 samples/sec
  CD music: 44,100 samples/sec
each sample quantized, i.e., rounded
  e.g., 28=256 possible quantized values
  each quantized value represented by bits, e.g., 8 bits for 256 values
time
audio signal amplitude
analog
signal
quantized value of analog value
quantization
error
sampling rate (N sample/sec)
Multimedia Networking 9-1

## Slide 4: Multimedia: audio
example: 8,000 samples/sec, 256 quantized values: 64,000 bps
receiver converts bits back to analog signal:
  some quality reduction
example rates
CD: 1.411 Mbps
MP3: 96, 128, 160 kbps
Internet telephony: 5.3 kbps and up
time
audio signal amplitude
analog
signal
quantized value of analog value
quantization
error
sampling rate (N sample/sec)
Multimedia Networking 9-1

## Slide 5: Multimedia: video
video: sequence of images displayed at constant rate
  e.g., 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy
within and between
images to decrease # bits used to encode image
spatial (within image)
temporal (from one image to next)
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i
frame i+1
Multimedia Networking 9-5

## Slide 6: Multimedia: video
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i
CBR: (constant bit rate): video encoding rate fixed
VBR: (variable bit rate): video encoding rate changes as amount of spatial, temporal coding changes
examples:
  MPEG 1 (CD-ROM) 1.5 Mbps
MPEG2 (DVD) 3-6 Mbps
MPEG4 (often used in Internet, < 1 Mbps)

## Slide 7: Multimedia networking: 3 application types
streaming, stored audio, video
  streaming: can begin playout before downloading entire file
  stored (at server): can transmit faster than audio/video will be rendered (implies storing/buffering at client)
  e.g., YouTube, Netflix, Hulu
conversational voice/video over IP
  interactive nature of human-to-human conversation limits delay tolerance
  e.g., Skype
streaming live audio, video
  e.g., live sporting event (futbol)

## Slide 8: Multimedia networking: outline
  multimedia networking applications
  streaming stored video
  voice-over-IP
  protocols for real-time conversational applications
  network support for multimedia

## Slide 9: Streaming stored video:
1. video recorded (e.g., 30 frames/sec)
2. video sent
Cumu
streaming: at this time, client playing out early part of video, while server still sending later part of video
network delay (fixed in this example)
time
3. video received, played out at client
(30 frames/sec)

## Slide 10: Streaming stored video: challenges
continuous playout constraint: once client playout begins, playback must match original timing
  … but network delays are variable (jitter), so will need client-side buffer to match playout requirements
other challenges:
  client interactivity: pause, fast-forward, rewind, jump through video
  video packets may be lost, retransmitted

## Slide 11: Streaming stored video: revisited
constant bit
rate video transmission
Cumu
time
variable network delay
client video
reception
constant bit rate video
playout at client
client playout delay
buffered video
client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 12: Client-side buffering, playout
variable fill rate, x(t)
client application buffer, size B
playout rate, e.g., CBR r
buffer fill level,
Q(t)
video server
client

## Slide 13: Client-side buffering, playout
variable fill rate, x(t)
client application buffer, size B
playout rate, e.g., CBR r
buffer fill level,
Q(t)
video server
client
Initial fill of buffer until playout begins at tp
playout begins at tp,
buffer fill level varies over time as fill rate x(t) varies and playout rate r is constant

## Slide 14: Client-side buffering, playout
playout buffering: average fill rate (x), playout rate (r):
x < r: buffer eventually empties (causing freezing of video playout until buffer again fills)
x > r: buffer will not empty, provided initial playout delay is large enough to absorb variability in x(t)
  initial playout delay tradeoff: buffer starvation less likely with larger delay, but larger delay until user
begins watching
variable fill rate, x(t)
client application buffer, size B
playout rate, e.g., CBR r
buffer fill level,
Q(t)
video server
Multimedia Networking 9-14

## Slide 15: Streaming multimedia: UDP
3 distinguishing properties of UDP:
  server sends at rate appropriate for client
    often: send rate = encoding rate = constant rate; Say, consumption rate=200 Mbps, UDP pacaket carries 8000 bits of video: 8000 bits/2Mbps = 4 msec Server transmit rate)
  Server encapsulates the video chunks (RTP) within transport packets before passing to UDP
  Server maintains Parallel control connection (pause, resume..)
transmission rate can be oblivious to congestion levels
short playout delay (2-5 seconds) to remove network jitter
error recovery: application-level, time permitting
RTP [RFC 2326]: multimedia payload types
3 Significant drawbacks of UDP:
Varying BW,
Need media control server (RTSP server),
Firewall (UDP may not go through firewalls)

## Slide 16: Streaming multimedia: HTTP
On client side bytes are collected at the application buffer
After predefined threshold, client app begins playback (read, decompress frames, display on the user screen)
Fill rate fluctuates due to TCP congestion control, retransmissions (in-order delivery)
Larger playout delay: smooth TCP delivery rate
HTTP/TCP passes more easily through firewalls
In HTTP streaming, video is stored in HTTP server (with specific url)
TCP connection
Multimedia file retrieved via HTTP GET (for that url)
Send at maximum possible rate under TCP
Server sends video file within the HTTP response message
variable rate, x(t)
TCP send buffer
video file
TCP receive buffer
application playout buffer
server
client

## Slide 17: Multimedia networking: outline
  multimedia networking applications
  streaming stored video
  voice-over-IP
  protocols for real-time conversational applications
  network support for multimedia

## Slide 18: Voice-over-IP (VoIP)
VoIP end-end-delay requirement: needed to maintain “conversational” aspect
  higher delays noticeable, impair interactivity
  < 150 msec: good
  > 400 msec bad
  includes application-level (packetization, playout), network delays
session initialization: how does callee advertise IP address, port number, encoding algorithms?
value-added services: call forwarding, screening, recording
emergency services: 911

## Slide 19: VoIP characteristics
speaker’s audio: alternating talk spurts, silent periods.
  64 kbps during talk spurt
  pkts generated only during talk spurts
  20 msec chunks at 8 Kbytes/sec: 160 bytes of data
application-layer header added to each chunk
chunk+header encapsulated into UDP or TCP segment
application sends segment into socket every 20 msec during talkspurt

## Slide 20: VoIP: packet loss, delay
network loss: IP datagram lost due to network congestion (router buffer overflow)
delay loss: IP datagram arrives too late for playout at receiver
  delays: processing, queueing in network; end- system (sender, receiver) delays
  typical maximum tolerable delay: 400 ms
loss tolerance: depending on voice encoding, loss concealment, packet loss rates between 1% and 10% can be tolerated

## Slide 21: Delay jitter
constant bit
rate transmission
Cumu
time
variable network delay (jitter)
client
reception
constant bit rate playout
at client
client playout delay
buffered data
end-to-end delays of two consecutive packets: difference can be more or less than 20 msec (transmission time difference)

## Slide 22: VoIP: fixed playout delay
receiver attempts to playout each chunk exactly q msecs after chunk was generated.
  chunk has time stamp t: play out chunk at
t+q
  chunk arrives after t+q: data arrives too late for playout: data “lost”
tradeoff in choosing q:
  large q: less packet loss
  small q: better interactive experience

## Slide 23: VoIP: fixed playout delay
sender generates packets every 20 msec during talk spurt
first packet received at time r
first playout schedule: begins at p
second playout schedule: begins at p’

## Slide 24: Adaptive playout delay (1)
goal: low playout delay, low late loss rate
approach: adaptive playout delay adjustment:
  estimate network delay, adjust playout delay at beginning of each talk spurt
  silent periods compressed and elongated
  chunks still played out every 20 msec during talk spurt
adaptively estimate packet delay: (EWMA -
exponentially weighted moving average, recall TCP
RTT estimadtei )=: (1-a)di-1 + a (ri – ti)
delay estimate after ith packet
small constant,
e.g. 0.1
time received - time sent
(timestamp)
measured delay of ith packet

## Slide 25: Adaptive playout delay (2)
also useful to estimate average deviation of delay, v
vi = (1-b)vi-1 + b |ri – ti – di|
estimates di, vi calculated for every received packet, but used only at start of talk spurt
for first packet in talk spurt, playout time is:
playout-timei = ti + di + Kvi
remaining packets in talkspurt are played out periodically

## Slide 26: Adaptive playout delay (3)
Q: How does receiver determine whether packet is first in a talkspurt?
if no loss, receiver looks at successive timestamps
  difference of successive stamps > 20 msec -->talk spurt begins.
with loss possible, receiver must look at both time stamps and sequence numbers
  difference of successive stamps > 20 msec and sequence numbers without gaps --> talk spurt begins.

## Slide 27: VoiP: recovery from packet loss
(1)
Challenge: recover from packet loss given small tolerable delay between original transmission and playout
each ACK/NAK takes ~ one RTT
alternative: Forward Error Correction (FEC)
  send enough bits to allow recovery without retransmission (recall two-dimensional parity in Ch. 5)
simple FEC
for every group of n chunks, create redundant chunk by exclusive OR-ing n original chunks
send n+1 chunks, increasing bandwidth by factor 1/n
can reconstruct original n chunks if at most one lost
chunk from n+1 chunks, with playout delay
Multimedia Networking 9-27

## Slide 28: VoiP: recovery from packet loss
(2)
another FEC scheme:
“piggyback lower quality stream”
send lower resolution audio stream as
redundant information
e.g., nominal
stream PCM at 64 kbps and redundant stream GSM at 13 kbps
  non-consecutive loss: receiver can conceal loss
  generalization: can also append (n-1)st and (n-2)nd low-bit r chunk
Multimedia Networking 9-28

## Slide 29: VoiP: recovery from packet loss (3)
interleaving to conceal loss:
audio chunks divided into smaller units, e.g. four 5 msec units per 20 msec audio chunk
packet contains small units from different chunks
if packet lost, still have most of every original chunk
no redundancy overhead, but increases playout delay
Multimedia Networking 9-29

## Slide 30: Voice-over-IP: Skype
proprietary application-
Skype clients (SC)
call
layer protocol (inferred via reverse engineering)
encrypted msgs
P2Pcliceonmtsp: oSnkeynptes:peers connect directly to each other for VoIP
super nodes (SN): Skype peers with special functions
overlay network: among SNs to locate SCs
login server
Skype login server
supernode (SN)
supernode overlay network

## Slide 31: P2P voice-over-IP: Skype
Skype client
1o. jpoeinrsaStiokynp:e network by
contacting SN (IP address cached) using
TloCgPs-in (username, password) to centralized Skype login
soebrtvaeinr s IP address for callee from SN, SN overlay
  or client buddy list
initiate call directly to callee
Skype login server

## Slide 32: Skype: peers as relays
problem: both Alice, Bob are behind “NATs”
  NAT prevents outside peer from initiating connection to insider peer
  inside peer can initiate connection to outside
relay solution: Alice, Bob maintain open connection to their SNs
  Alice signals her SN to connect to Bob
  Alice’s SN connects to Bob’s SN
  Bob’s SN connects to Bob over open connection Bob initially initiated to his SN

## Slide 33: Multimedia networking: outline
  multimedia networking applications
  streaming stored video
  voice-over-IP
  protocols for real-time conversational applications: RTP, SIP
  network support for multimedia

## Slide 34: Real-Time Protocol (RTP)
RTP specifies packet structure for packets carrying audio, video data
RFC 3550
RTP packet provides
  payload type identification
  packet sequence numbering
  time stamping
RTP runs in end systems
RTP packets encapsulated in UDP segments
interoperability: if two VoIP applications run RTP, they may be able to work together

## Slide 35: RTP runs on top of UDP
RTP libraries provide transport-layer interface that extends UDP:
port numbers, IP addresses
payload type identification
packet sequence numbering
time-stamping

## Slide 36: RTP example
example: sending 64 kbps PCM-encoded voice over RTP
application collects encoded data in chunks, e.g., every 20 msec = 160 bytes in a chunk
audio chunk + RTP header form RTP packet, which is encapsulated in UDP segment
RTP header indicates type of audio encoding in each packet
  sender can change encoding during conference
RTP header also contains sequence numbers, timestamps

## Slide 37: RTP and QoS
RTP does not provide any mechanism to ensure timely data delivery or other QoS guarantees
RTP encapsulation only seen at end systems (not by intermediate routers)
  routers provide best-effort service, making no special effort to ensure that RTP packets arrive at destination in timely matter

## Slide 38: RTP header
payload type | sequence number | time stamp | Synchronization Source ID | Miscellaneous fields
type
payload type (7 bits): indicates type of encoding currently being
used. If sender changes encoding during call, sender informs receiver via payload type field
Payload type 0: PCM mu-law, 64 kbps
Payload type 3: GSM, 13 kbps
Payload type 7: LPC, 2.4 kbps Payload type 26: Motion JPEG Payload type 31: H.261 Payload type 33: MPEG2 video
sequence # (16 bits): increment by one for each RTP packet sent
detect packet loss, restore packet sequenMucltiemedia Networking 9-38

## Slide 39: RTP header
timestamp field (32 bits long): sampling instant of first byte in this RTP data packet
  for audio, timestamp clock increments by one for each sampling period (e.g., each 125 usecs for 8 KHz sampling clock)
  if application generates chunks of 160 encoded samples, timestamp increases by 160 for each RTP packet when source is active. Timestamp clock continues to increase at constant rate when source is inactive.
SSRC field (32 bits long): identifies source of RTP stream. Each stream in RTP session has distinct
SSRC
payload type | sequence number | time stamp | Synchronization Source ID | Miscellaneous fields
type
Multimedia Networking 9-39

## Slide 40: RTSP/RTP programming assignment
build a server that encapsulates stored video frames into RTP packets
  grab video frame, add RTP headers, create UDP segments, send segments to UDP socket
  include seq numbers and time stamps
  client RTP provided for you
also write client side of RTSP
  issue play/pause commands
  server RTSP provided for you

## Slide 41: Real-Time Control Protocol (RTCP)
works in conjunction with RTP
each participant in RTP session periodically sends RTCP control packets to all other participants
each RTCP packet contains sender and/or receiver reports
  report statistics useful to application: # packets sent, # packets lost, interarrival jitter
feedback used to control performance
  sender may modify its transmissions based on feedback

## Slide 42: RTCP: multiple multicast senders
RTCP
RTP
RTCP
RTCP
sender
receivers
each RTP session: typically a single multicast address; all RTP /RTCP packets belonging to session use multicast address
RTP, RTCP packets distinguished from each other via distinct port numbers
to limit traffic, each participant reduces RTCP traffic as number of conference participants increasesMultimedia Networking 9-42

## Slide 43: RTCP: packet types
receiver report packets:
fraction of packets lost, last sequence number, average interarrival jitter
sender report packets:
SSRC of RTP stream, current time, number of packets sent, number of bytes sent
source description packets:
e-mail address of sender, sender's name, SSRC of associated RTP stream
provide mapping between the SSRC and the user/host name

## Slide 44: RTCP: stream synchronization
RTCP can synchronize different media streams within a RTP session
e.g., videoconferencing app: each sender generates one RTP stream for video, one for audio.
timestamps in RTP packets tied to the video, audio sampling clocks
  not tied to wall-clock time
each RTCP sender- report packet contains (for most recently generated packet in associated RTP stream):
  timestamp of RTP packet
  wall-clock time for when packet was created
receivers uses association to synchronize playout of audio, video

## Slide 45: RTCP: bandwidth scaling
RTCP attempts to limit its traffic to 5% of session bandwidth
example : one sender, sending video at 2 Mbps
RTCP attempts to limit RTCP traffic to 100 Kbps
RTCP gives 75% of rate to receivers; remaining 25% to sender
75 kbps is equally shared among receivers:
  with R receivers, each receiver gets to send RTCP traffic at 75/R kbps.
sender gets to send RTCP traffic at 25 kbps.
participant determines RTCP packet transmission period by calculating avg RTCP packet size (across entire session) and dividing by allocated rate

## Slide 46: SIP: Session Initiation Protocol [RFC 3261]
long-term vision:
all telephone calls, video conference calls take place over Internet
people identified by names or e-mail addresses, rather than by phone numbers
can reach callee (if callee so desires), no matter where callee roams, no matter what IP device callee is currently using

## Slide 47: SIP services
SIP provides mechanisms for call setup:
  for caller to let callee know she wants to establish a call
  so caller, callee can agree on media type, encoding
  to end call
determine current IP address of callee:
  maps mnemonic identifier to current IP address
call management:
  add new media streams during call
  change encoding during call
  invite others
  transfer, hold calls

## Slide 48: Example: setting up call to known IP address
Alice’s SIP invite message indicates her port number, IP address, encoding she prefers to receive (PCM law)

Bob’s 200 OK message
indicates his port number, IP address, preferred encoding (GSM)

SIP messages can be
sent over TCP or UDP; here sent over RTP/UDP

default SIP port number
is 5060

## Slide 49: Setting up a call (more)
codec negotiation:
  suppose Bob doesn’t have PCM law encoder
  Bob will instead reply with 606 Not Acceptable Reply, listing his encoders. Alice can then send new INVITE message, advertising different encoder
rejecting a call
  Bob can reject with replies “busy,” “gone,” “payment required,” “forbidden”
media can be sent over RTP or some other protocol

## Slide 50: Example of SIP message
INVITE sip:bob@domain.com SIP/2.0 Via: SIP/2.0/UDP 167.180.112.24
From: sip:alice@hereway.com To: sip:bob@domain.com
Call-ID: a2e3a@pigeon.hereway.com Content-Type: application/sdp Content-Length: 885
c=IN IP4 167.180.112.24
m=audio 38060 RTP/AVP 0
Notes:
HTTP message syntax
sdp = session description protocol
Call-ID is unique for every call
Here we don’t know Bob’s IP address
  intermediate SIP
Asleicrevesresnndese, ded
receives SIP messages using SIP default port 506
Alice specifies in
header that SIP client sends, receives SIP
mesMsultaimgedeia sNetowovrkeingr9-50

## Slide 51: Name translation, user location
caller wants to call callee, but only has callee’s name or e- mail address.
need to get IP address of callee’s current host:
  user moves around
  DHCP protocol
  user has different IP devices (PC, smartphone, car device)
result can be based on:
  time of day (work, home)
  caller (don’t want boss to call you at home)
  status of callee (calls sent to voicemail when callee is already talking to someone)

## Slide 52: SIP registrar
REGISTER sip:domain.com SIP/2.0
Via: SIP/2.0/UDP 193.64.210.89
From: sip:bob@domain.com To: sip:bob@domain.com Expires: 3600
one function of SIP server: registrar
when Bob starts SIP client, client sends SIP REGISTER message to Bob’s registrar server
register message:

## Slide 53: SIP proxy
another function of SIP server: proxy
Alice sends invite message to her proxy server
  contains address sip:bob@domain.com
  proxy responsible for routing SIP messages to callee, possibly through multiple proxies
Bob sends response back through same set of SIP proxies
proxy returns Bob’s SIP response message to Alice
  contains Bob’s IP address
SIP proxy analogous to local DNS server plus TCP setup

## Slide 54: SIP example: jim@umass.edu calls keith@poly.edu
1
1. Jim sends INVITE message to UMass SIP proxy.
2. UMass proxy forwards request to Poly registrar server
2
3. Poly server returns redirect response, indicating that it should try keith@eurecom.fr
3
5. eurecom registrar forwards INVITE to 197.87.54.21, which is running keith’s SIP client
5
4
4. Umass proxy forwards request
8
6
to Eurecom registrar server
7
6-8. SIP response returned to Jim
9
9. Data flows between clients
UMass
SIP proxy
Poly SIP
registrar
Eurecom SIP registrar
197.87.54.21
128.119.40.186

## Slide 55: Comparison with H.323
H.323: another signaling protocol for real-time, interactive multimedia
H.323: complete, vertically integrated suite of protocols for multimedia conferencing: signaling, registration, admission control, transport, codecs
SIP: single component. Works with RTP, but does not mandate it. Can be combined with
H.323 comes from the ITU (telephony)
SIP comes from IETF: borrows much of its concepts from HTTP
  SIP has Web flavor;
H.323 has telephony flavor
SIP uses KISS principle: Keep It Simple Stupid
Multimedia Networking 9-55

## Slide 56: Multimedia networking: outline
  multimedia networking applications
  streaming stored video
  voice-over-IP
  protocols for real-time conversational applications
  network support for multimedia

## Slide 57: Network support for multimedia

## Slide 58: Dimensioning best effort networks
approach: deploy enough link capacity so that congestion doesn’t occur, multimedia traffic flows without delay or loss
  low complexity of network mechanisms (use current “best effort” network)
  high bandwidth costs
challenges:
  network dimensioning: how much bandwidth is “enough?”
  estimating network traffic demand: needed to determine how much bandwidth is “enough” (for that much traffic)

## Slide 59: Providing multiple classes of service
0111
thus far: making the best of best effort service
  one-size fits all service model
alternative: multiple classes of service
  partition traffic into classes
  network treats different classes of traffic differently (analogy: VIP service versus regular service)
granularity: differential service among
multiple classes, not among individual connections
history: ToS bits

## Slide 60: Multiple classes of service: scenario
R1
R2
H1
H2
H3
H4
1.5 Mbps link
R1 output interface queue

## Slide 61: Scenario 1: mixed HTTP and VoIP
example: 1Mbps VoIP, HTTP share 1.5 Mbps link.
  HTTP bursts can congest router, cause audio loss
  want to give priority to audio over HTTP
Principle 1
packet marking needed for router to distinguish between different classes; and new router policy to treat packets accordingly
R1
R2

## Slide 62: Principles for QOS guarantees (more)
what if applications misbehave (VoIP sends higher than declared rate)
  policing: force source adherence to bandwidth allocations
marking, policing at network edge
R1
R2
1 Mbps phone
1.5 Mbps link
packet marking and policing
Principle 2
provide protection (isolation) for one class from others

## Slide 63: Principles for QOS guarantees (more)
allocating fixed (non-sharable) bandwidth to flow: inefficient use of bandwidth if flows doesn’t use its allocation
Principle 3
while providing isolation, it is desirable to use resources as efficiently as possible
R1
R2
1 Mbps phone
1 Mbps logical link
1.5 Mbps link
0.5 Mbps logical link

## Slide 64: Scheduling and policing mechanisms
packet scheduling: choose next queued packet to send on outgoing link
previously covered in Chapter 4:
  FCFS: first come first served
  simply multi-class priority
  round robin
  weighted fair queueing (WFQ)
queue (waiting area)
packet arrivals
packet departures
link (server)

## Slide 65: Policing mechanisms
goal: limit traffic to not exceed declared parameters
Three common-used criteria:
(long term) average rate: how many pkts can be sent per unit time (in the long run)
  crucial question: what is the interval length: 100 packets per sec or 6000 packets per min have same average!
peak rate: e.g., 6000 pkts per min (ppm) avg.; 1500 ppm peak rate
(max.) burst size: max number of pkts sent consecutively (with no intervening idle)

## Slide 66: Policing mechanisms: implementation
token bucket: limit input to specified burst size
and average rate
bucket can hold b tokens
tokens generated at rate r token/sec unless bucket full
over interval of length t: number of packets admitted less than or equal to (r t + b)

## Slide 67: Policing and QoS guarantees
token bucket, WFQ combine to provide guaranteed upper bound on delay, i.e., QoS guarantee!
token rate, r
bucket size, b
per-flow rate, R
WFQ
D = b/R max
arriving traffic
arriving traffic

## Slide 68: Differentiated services
want “qualitative” service classes
  “behaves like a wire”
  relative service distinction: Platinum, Gold, Silver
scalability: simple functions in network core, relatively complex functions at edge routers (or hosts)
  signaling, maintaining per-flow router state difficult with large number of flows
don’t define define service classes, provide functional components to build service classes

## Slide 69: Diffserv architecture
edge router:
per-flow traffic management
marks packets as in- profile and out-profile
core router:
per class traffic management
buffering and scheduling based on marking at edge
preference given to in-profile packets over out-of-profile packets
r
b
marking
scheduling
.
.

## Slide 70: Edge-router packet marking
profile: pre-negotiated rate r, bucket size b
packet marking at edge based on per-flow
profile
rate r
b
user packets
possible use of marking:
class-based marking: packets of different classes marked differently
intra-class marking: conforming portion of flow marked differently than non-conforming one

## Slide 71: Diffserv packet marking: details
packet is marked in the Type of Service (TOS) in IPv4, and Traffic Class in IPv6
6 bits used for Differentiated Service Code Point (DSCP)
  determine PHB that the packet will receive
  2 bits currently unused
DSCP |  |  |  |  |  | unused | 

## Slide 72: Classification, conditioning
may be desirable to limit traffic injection rate of some class:
user declares traffic profile (e.g., rate, burst size)
traffic metered, shaped if non-conforming

## Slide 73: Forwarding Per-hop Behavior (PHB)
PHB result in a different observable (measurable) forwarding performance behavior
PHB does not specify what mechanisms to use to ensure required PHB performance behavior
examples:
  class A gets x% of outgoing link bandwidth over time intervals of a specified length
  class A packets leave first before packets from class B

## Slide 74: Forwarding PHB
PHBs proposed:
expedited forwarding: packet departure rate of a class equals or exceeds specified rate
  logical link with a minimum guaranteed rate
assured forwarding: 4 classes of traffic
  each guaranteed minimum amount of bandwidth
  each with three drop preference partitions

## Slide 75: Per-connection QOS guarantees
basic fact of life: can not support traffic demands beyond link capacity
Principle 4
call admission: flow declares its needs, network may block call (e.g., busy signal) if it cannot meet needs
R1
R2
1.5 Mbps link
1 Mbps phone
1 Mbps phone

## Slide 76: QoS guarantee scenario
resource reservation
  call setup, signaling (RSVP)
  traffic, QoS declaration
  per-element admission control
request/ reply
QoS-sensitive scheduling
(e.g., WFQ)

## Slide 77: Multimedia networking: outline
  multimedia networking applications
  streaming stored video
  voice-over-IP
  protocols for real-time conversational applications
  network support for multimedia