## Slide 1: Chapter 4 Network Layer: The Data Plane
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify,
and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this
material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top Down Approach
7th edition
Jim Kurose, Keith Ross
Pearson/Addison Wesley April 2016
Network Layer: Data Plane 4-1

## Slide 2: Chapter 4: outline
  Overview of Network layer
    data plane
    control plane
  What’s inside a router
  IP: Internet Protocol
    datagram format
    fragmentation
    IPv4 addressing
    network address translation
    IPv6
Network Layer: Data Plane 4-1
  Generalized Forward and SDN
    match
    action
    OpenFlow examples of match-plus-action in action

## Slide 3: Chapter 4: network layer
Network Layer: Data Plane 4-1
chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  generalized forwarding
instantiation, implementation in the Internet

## Slide 4: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing
application
transport
network
data link
physical
application
transport
k
networ
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
work
net
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
Network Layer: Data Plane 4-4

## Slide 5: Two key network-layer functions
network-layer functions:
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to destination
  routing algorithms
analogy: taking a trip
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination
Network Layer: Data Plane 4-5

## Slide 6: Network layer: data plane, control plane
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote)
servers
2
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
values in arriving packet header
0111 1
3
Network Layer: Data Plane 4-6

## Slide 7: Per-router control plane (Traditional Approa
Routing Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data plane
control plane
1
2
0111
values in arriving packet header
Network Layer: Control Plane 5-7
3

## Slide 8: Logically centralized control plane
control plane
data plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
Network Layer: Control Plane 5-7
values in arriving packet header

## Slide 9: Network service model
Q: What service model for “channel” transporting datagrams from sender to
receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 10: Network layer service models:
Network Architecture | Service Model | Bandwidth | Guarantees ? Loss Order Timing |  |  | Congestion feedback
Internet | best effort | none | no | no | no | no (inferred
 |  |  |  |  |  | via loss)
ATM | CBR | constant rate | yes | yes | yes | no congestion
ATM | VBR | guaranteed rate | yes | yes | yes | no congestion
ATM | ABR | guaranteed minimum | no | yes | no | yes
ATM | UBR | none | no | yes | no | no

## Slide 11: Chapter 4: outline
  Overview of Network layer
    data plane
    control plane
  What’s inside a router
  IP: Internet Protocol
    datagram format
    fragmentation
    IPv4 addressing
    network address translation
    IPv6
  Generalized Forward and SDN
    match
    action
    OpenFlow examples of match-plus-action in action

## Slide 12: Router architecture overview
high-seed switching fabric
routing processor
router input ports
router output ports
forwarding data plane
(hardware) operttes in
nanosecond timeframe
routing, management control plane (software) operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 13: Input port functions
line termination
link layer protocol (receive)
lookup, forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer: bit-level reception
data link layer: e.g., Ethernet see chapter 5
switch fabric

## Slide 14: Input port functions
line termination
link layer protocol (receive)
lookup, forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based
physical layer: bit-level reception
data link layer: e.g., Ethernet see chapter 5
switch fabric

## Slide 15: Destination-based
Destination Address Range |  |  |  | Link Interface
11001000 | 00010111 | 00010000 | 00000000 | 
through |  |  |  | 0
11001000 | 00010111 | 00010111 | 11111111 | 
11001000 | 00010111 | 00011000 | 00000000 | 
through |  |  |  | 1
11001000 | 00010111 | 00011000 | 11111111 | 
11001000 through | 00010111 | 00011001 | 00000000 | 2
11001000 | 00010111 | 00011111 | 11111111 | 
otherwise |  |  |  | 3
Q: but what happens if ranges don’t divide up so nicely?
forwarding
forwarding table
Network Layer: Data Plane 4-15

## Slide 16: Longest prefix matching
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface? which interface?
Destination Address Range | Link interface
11001000 00010111 00010*** ********* | 0
11001000 00010111 00011000 ********* | 1
11001000 00010111 00011*** ********* | 2
otherwise | 3
longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.

## Slide 17: Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: can up ~1M routing table entries in TCAM

## Slide 18: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 19: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input port (e.g., Ethernet)
memory
output port (e.g., Ethernet)
system bus

## Slide 20: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 21: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 22: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention: only one red datagram can be
transferred.
lower red packet is blocked
switch fabric
one packet time later: green packet experiences HOL blocking
switch fabric

## Slide 23: Output ports
buffering requir
ed when datagrams faster than the
scheduli
queued d
ng discipline chooses among atagrams for transmission
line termination
link layer protocol (send)
switch fabric
datagram buffer
queueing
This slide in HUGELY important!
Datagram (packets) can be lost
arrive from fabric due to congestion, lack of buffers
transmission rate
Priority scheduling – who gets best performance, network neutrality

## Slide 24: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more from input to output
one packet time later
switch fabric
switch fabric

## Slide 25: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT . C
N

## Slide 26: Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example?
  discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly
queue (waiting area)
packet arrivals
packet departures
link (server)

## Slide 27: Scheduling policies: priority
priority scheduling: send highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc.
  real world example?
high priority queue
(waiting area)
(waiting area)
arrivals
departures
classify link
low priority queue (server)
1
3 2 4
5
5
5
2
1
3
1 3 2 4
4
arrivals
departures
packet in service

## Slide 28: Scheduling policies: still more
1
3
2 4
5
5
5
Round Robin (RR) scheduling:
multiple classes
cyclically scan class queues, sending one complete packet from each class (if available)
real world example?
2
3
1 3 3 4
1 4
arrivals
departures
packet in service

## Slide 29: Scheduling policies: still more
Weighted Fair Queuing (WFQ):
generalized Round Robin
each class gets weighted amount of service in each cycle
real-world example?

## Slide 30: Chapter 4: outline
  Overview of Network layer
    data plane
    control plane
  What’s inside a router
  IP: Internet Protocol
    datagram format
    fragmentation
    IPv4 addressing
    network address translation
    IPv6
  Generalized Forward and SDN
    match
    action
    OpenFlow examples of match-plus-action in action

## Slide 31: The Internet network layer
host, router network layer functions:
transport layer: TCP, UDP
routing protocols IP protocol path selection • addressing conventions RIP, OSPF, BGP • datagram format packet handling conventions forwarding table ICMP protocol • error reporting router “signaling”
link layer
physical layer
network
layer

## Slide 32: IP datagram format
length
32 bits
data (variable length, typically a TCP or UDP segment)
header
checksum
time to live
32 bit source IP address
ver head. type of
len service
16-bit identifier
flgs
fragment offset
upper layer
32 bit destination IP address
options (if any)
IP protocol version
total datagram length (bytes)
for fragmentation/ reassembly
number header length
(bytes) “type” of data
max number remaining hops (decremented at each router)
upper layer protocol to deliver payload to
e.g. timestamp, record route taken, specify list of routers to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
 = 40 bytes + app layer overhead

## Slide 33: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link- level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
“reassembled” only at final destination
IP header bits used to identify, order
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
Network Layer: Data Plane 4-33
1500 bytes link
4000 bytes Datagram
A Large Datagram – 4000 bytes
(20 byte header plus 3980 bytes pay load);
MTU – 1500 bytes implies 3980 bytes be in 3 separate fragments (multiple of 8 byte chunk => 8x185=1480 bytes;

## Slide 34: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
offset
=185
fragflag
=1
length
=1500 =x
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes several (3) smaller datagrams
1480 bytes in data field
offset =
1480/8
A Large Datagram – 4000 bytes
(20 byte header plus 3980 bytes pay load); MTU – 1500 bytes implies 3980 bytes be in
3 separate fragments (multiple of 8 byte chunk => 8x185=1480 bytes in payload;
Meaning data should be Inserted beginning at byte 0)
Meaning data should be Inserted beginning at byte 1480 (note 185 x.8 = 1480)
Meaning data should be Inserted beginning at byte 2960 (note 370 x.8 = 2960)
1020 bytes in data field (pay load) + 20 bytes in header => 1040 bytes
A Large Datagram – 4000 bytes
(20 byte header plus 3980 bytes pay load); MTU – 1500 bytes implies 3980 bytes be in
3 separate fragments (multiple of 8 byte chunk => 8x185=1480 bytes;
example:
4000 byte datagram
MTU = 1500 bytes

## Slide 35: Chapter 4: outline
  Overview of Network layer
    data plane
    control plane
  What’s inside a router
  IP: Internet Protocol
    datagram format
    fragmentation
    IPv4 addressing
    network address translation
    IPv6
  Generalized Forward and SDN
    match
    action
    OpenFlow examples of match-plus-action in action

## Slide 36: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223 1 1 1

## Slide 37: IP addressing: introduction
Q: how are interfaces actually connected?
A: we’ll learn about that in chapter 5, 6.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)

## Slide 38: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.1
223.1.1.2
223.1.2.2
223.1.3.27
subnet
223.1.3.2
223.1.2.1

## Slide 39: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.3.0/24
223.1.1.3
223.1.3.2
223.1.3.1
subnet
 | 223.1.2.0/24
223.1.1.1 | 
223.1.1.2 | 223.1.2.1
223.1.1.4 | 223.1.2.9
223.1.3.27
223.1.2.2

## Slide 40: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.1 223.1.8.0
223.1.9.1
223.1.9.2

## Slide 41: IP addressing: CIDR
CIDR: Classless InterDomain Routing
subnet portion of address of arbitrary length
address format: a.b.c.d/x, where x is # bits in subnet portion of address
subnet part
host part
11001000 00010111 00010000 00000000
200.23.16.0/23

## Slide 42: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration-
>tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 43: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
can renew its lease on address in use
allows reuse of addresses (only hold address while connected/“on”)
support for mobile users who want to join network (more shortly)
DHCP overview:
host broadcasts “DHCP discover” msg [optional]
DHCP server responds with “DHCP offer” msg [optional]
host requests IP address: “DHCP request” msg
DHCP server sends address: “DHCP ack” msg

## Slide 44: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP client needs address in this network

## Slide 45: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 46: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
address of first-hop router for client
name and IP address of DNS sever
network mask (indicating network versus host portion of address)

## Slide 47: DHCP: example
router with DHCP server built into router
DHCP
) on LAN,
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1
Ethernet frame broadcast (dest: FFFFFFFFFFFF received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 48: DHCP: example
router with DHCP server built into router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS
esenrcvaeprsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
client now knows its IP address, name and IP address of DSN server, IP address of its first- hop router

## Slide 49: DHCP: Wireshark output
Message type: Boot Reply (2) Hardware type: Ethernet Hardware address length: 6 Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a) Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK Option: (t=54,l=4) Server Identifier = 192.168.1.1 Option: (t=1,l=4) Subnet Mask = 255.255.255.0 Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092; IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
(home LAN)
Message type: Boot Request (1) Hardware type: Ethernet Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast) Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given Boot file name not given Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A; Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101 Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name 3 = Router; 6 = Domain Name Server 44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 50: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block
11001000 00010111 00010000 00000000 200.23.16.0/20
0 00000000 200.23.16.0/23
0 00000000 200.23.18.0/23
0 00000000 200.23.20.0/23
…. ….
11001000 00010111 00011110 00000000 200.23.30.0/23
11001000 | 00010111 | 0001 | 000
11001000 | 00010111 | 0001 | 001
11001000 | 00010111 | 0001 | 010
…..
Organization 0
Organization 1
Organization 2
...
Organization 7

## Slide 51: Hierarchical addressing: route aggregation
“Send me anything with addresses beginning 200.23.16.0/20”
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
200.23.16.0/23
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything with addresses beginning 199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
hierarchical addressing allows efficient advertisement of routing information:

## Slide 52: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything with addresses beginning 200.23.16.0/20”
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
200.23.16.0/23
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything with addresses
beginning 199.31.0.0/16 or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.

## Slide 53: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
allocates addresses
manages DNS
assigns domain names, resolves disputes

## Slide 54: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
138.76.29.7
local network (e.g., home network)
10.0.0/24
10.0.0.4
rest of Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving
local network have same single source NAT IP
address: 138.76.29.7,different source port numbers
Network Layer: Data Plane 4-54

## Slide 55: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
range of addresses not needed from ISP: just one IP address for all devices
can change addresses of devices in local network without notifying outside world
can change ISP without changing addresses of devices in local network
devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 56: NAT: network address translation implementation: NAT router must:
outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
. . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 57: Fill out the blanks (?) for NAT
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
10.0.0.1
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to 128.119.40.186, 80
NAT translation table |  |  |  | 
WAN | side | addr |  | LAN side addr
 | ? |  |  | 0.0.0.1, 3345
…… |  |  |  | ……
S: ?
D: ?
4
S: ?
D: ?
2
2: ?
S: ?
D: ?
3
3: ?
4: ?

## Slide 58: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  address shortage should be solved by IPv6
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?

## Slide 59: Chapter 4: outline
  Overview of Network layer
    data plane
    control plane
  What’s inside a router
  IP: Internet Protocol
    datagram format
    fragmentation
    IPv4 addressing
    network address translation
    IPv6
  Generalized Forward and SDN
    match
    action
    OpenFlow examples of match-plus-action in action

## Slide 60: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 61: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.” (concept of“flow” not well defined).
next header: identify upper layer protocol for data
ver | pri | flow label |  | 
payload len |  |  | next hdr | hop limit
source address (128 bits) |  |  |  | 
destination address (128 bits) |  |  |  | 
data |  |  |  | 
32 bits

## Slide 62: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 63: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 header fields
IPv4 source, dest addr
IPv6 datagram IPv4 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 64: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 65: Tunneling
flow: X src: A dest: F
data
A-to-B: IPv6
Flow: X Src: A Dest: F
data
src:B dest: E
B-to-C:
IPv6 inside IPv4
E-to-F: IPv6
flow: X src: A dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X Src: A Dest: F
data
src:B dest: E
physical view:
A
B
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv6 IPv4
IPv4
Network Layer: Data Plane 4-65

## Slide 66: IPv6: adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
  Why?

## Slide 67: Chapter 4: outline
  Overview of Network layer
    data plane
    control plane
  What’s inside a router
  IP: Internet Protocol
    datagram format
    fragmentation
    IPv4 addressing
    network address translation
    IPv6
  Generalized Forward and SDN
    match
    action
    OpenFlow examples of match-plus-action in action

## Slide 68: Generalized Forwarding and SEDachNrouter contains a flow table that is computed and distributed by a logically centralized routing controller
2
3
values in arriving packet’s header
logically-centralized routing controller
1
 | 0100 | 1101
control plane
data plane
local flow table |  | 
headers | counters | actions

## Slide 69: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules

## Slide 70: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
1. src=1.2.*.*, dest=3.4.5.*  drop
2. src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard
Match –plus-action

## Slide 71: OpenFlow: Flow Table Entries
Rule
Action
Stats
Packet + byte counters Forward packet to port(s) Encapsulate and forward to controller Drop packet Send to normal processing pipeline Modify Fields |  |  |  |  |  |  |  |  | 
Switch Port | VLAN ID | MAC src | MAC dst | Eth type | IP Src | IP Dst | IP Prot | TCP sport | TCP dport
Link layer
Network layer
Transport layer

## Slide 72: Examples
Destination-based forwarding:
Switch Port | MAC src | MAC dst | Eth type | VLAN ID | IP Src | IP Dst | IP Prot | TCP sport | TCP dport | Action
* * *
* * *
51.6.0.8 *
* * port6
IP datagrams destined to IP address
51.6.0.8 should be forwarded to router output
port 6
Switch Port | MAC src | MAC dst | Eth type | VLAN ID | IP Src | IP Dst | IP Prot | TCP sport | TCP dport | Forward
Firewall:
* * * do * * * * * * 22 drop
not forward (block) all datagrams destined to TCP
port 22
Switch Port | MAC src | MAC dst | Eth type | VLAN ID | IP Src | IP Dst | IP Prot | TCP sport | TCP dport | Forward
* * *
128.119.1.1
* * * * * *
drop
do not forward (block) all datagrams sent by host
128.119.1.1

## Slide 73: Examples
Destination-based layer 2 (switch) forwarding:
*
Switch Port | MAC src | MAC dst | Eth type | VLAN ID | IP Src | IP Dst | IP Prot | TCP sport | TCP dport | Action
* * * *
* * * * port3
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to
output port 3
22:A7:23:
11:E1:02

## Slide 74: OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out
a link
Switch
  match: destination MAC address
  action: forward or
flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or
deny
NAT
  match: IP address and port
  action: rewrite
address and port
match+action: unifies different kinds of devices

## Slide 75
match | action
match | action
match | action
Host h1 10.1.0.1
Host h4
10.2.0.4
Host h2 10.1.0.2
Host h3 10.2.0.3
Host h5 10.3.0.5
s1
s2
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
s3
controller
Given Rules: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to
s2.
Complete all 3 Flow tables for s3, s2, and s1 in the diagram

## Slide 76: Chapter 4: done!
  Overview of Network layer: data plane and control plane
  What’s inside a router
  IP: Internet Protocol
    datagram format
    fragmentation
    IPv4 addressing
    NAT
    IPv6
  Generalized Forward and SDN
    match plus action
    OpenFlow example
Question: how do forwarding tables (destination-based forwarding) or flow tables (generalized forwarding) computed?
Answer: by the control plane (next chapter)
Network Layer: Data Plane 4-76